# chapter 3

## Findings of Fact Regarding Impacts

### 3.2	Significant Adverse Impacts Reduced to Less-than-Significant Level by Mitigation Measures Incorporated

The Draft EIR/EIS identifies significant impacts that would be reduced to a less-than-significant level by the inclusion of the mitigation measures identified in the Draft EIR/EIS for the approval of NBWRP.

#### Section 3.1 Geology and Seismicity

##### Impact 3.1.1 Seismicity

Impact 3.1.1: In the event of a major earthquake in the Bay Area Region, the proposed facilities could be subject to fault rupture, severe ground shaking, liquefaction, or earthquake induced landslides capable of causing injury, structural damage, pipeline rupture and service interruption.

##### Mitigation

The following mitigation measure is hereby adopted and will be implemented as set forth in the Mitigation Monitoring and Reporting Program (MMRP). This measure will mitigate the above impact to a less-than-significant level.

Mitigation Measure 3.1.1: The Member Agencies will implement the following measures:

- All proposed improvements will be designed and constructed in accordance with current geotechnical industry standard criteria, including the California Building Code (CBC) and American Waterworks Association (AWWA) criteria.

- The project construction materials and backfill materials will be designed according to a geotechnical investigation by a California-licensed geotechnical engineer or engineering geologist to address landslide, subsidence, liquefaction, and expansive soils and seismic hazards such as ground shaking and liquefaction.

- Implementation of industry standard geotechnical measures such as replacing excavated soils with engineered fill materials are effective means to overcome the potential for subsidence. If excavated soils are to be reused for backfill, they would still be appropriately compacted to mitigate the potential for subsidence or settlement and evaluated for expansion and amended, if necessary, to reduce the potential for expansion in accordance with accepted geotechnical practices.

- Proposed facilities will be designed to include flexible connections, where deemed necessary, along with backfill requirements that minimize the potential for significant damage. All other associated improvements will employ standard design and construction using the most recent geotechnical practices and California Building Code (CBC) seismic criteria, which would provide conservative design criteria.

##### Findings

Based on the EIR/EIS and the entire record before Napa County, the Board finds, in accordance with CEQA Section 15901(a)(1), that changes or alterations have been required in, or incorporated into, the project which avoid or substantially lessen the significant environmental effect as identified in the Final EIR.

##### Rationale

Incorporation of seismic criteria as it applies to the design of the project components including the WWTP improvements and the recycled water conveyance system would comply with the CBC. Implementation of standard geotechnical measures would mitigate the potential of geological hazards.

##### Impact 3.1.2 Erosion

Impact 3.1.2: Project construction activities could result in short-term erosion and loss of topsoils.

##### Mitigation

The following mitigation measure is hereby adopted and will be implemented as set forth in the MMRP. This measure will mitigate the above impact to a less-than-significant level.

Mitigation Measure 3.1.2: The Member Agencies will implement the following measures:

- Consistent with Stormwater Pollution Prevention Plan (SWPPP) requirements, the construction contractor shall be required to implement BMPs for erosion control onsite. The use of construction BMPs will minimize the potential for erosion and loss of topsoil, and shall include, without limitation, the following:

  - Avoid scheduling construction activities during a rain event, but be prepared for sudden changes in conditions;

  - Construct berms, silt fences, straw bales, fiber rolls, and/or sand bags around stockpiled soils;

  - Cover stockpiled soils during a rain event and monitor perimeter barriers, repair as necessary;

  - Stabilize entrances to work area to prevent tracking of dirt or mud onto roadways; and

- Implement dust control practices as appropriate on all stockpiled material.

##### Findings

Based on the EIR/EIS and the entire record before Napa County, the Board finds, in accordance with CEQA Section 15901(a)(1), that changes or alterations have been required in, or incorporated into, the project which avoid or substantially lessen the significant environmental effect as identified in the Final EIR.

##### Rationale

Implementation of BMPs would include soil erosion and stormwater runoff control measures and would minimize impacts erosion and loss of topsoil.

##### Impact 3.1.3 Unstable Soils

Impact 3.1.3: Project improvements could be located on a geologic unit or soil that is unstable that could potentially result in landslide, lateral spreading, subsidence, liquefaction or collapse causing damage to structures and service disruptions.

##### Mitigation

The following mitigation measure is hereby adopted and will be implemented as set forth in the MMRP. This measure will mitigate the above impact to a less-than-significant level.

Mitigation Measure 3.1.1: The Member Agencies will implement the following measures:

- All proposed improvements will be designed and constructed in accordance with current geotechnical industry standard criteria, including the California Building Code (CBC) and American Waterworks Association (AWWA) criteria.

- The project construction materials and backfill materials will be designed according to a geotechnical investigation by a California-licensed geotechnical engineer or engineering geologist to address landslide, subsidence, liquefaction, and expansive soils and seismic hazards such as ground shaking and liquefaction.

- Implementation of industry standard geotechnical measures such as replacing excavated soils with engineered fill materials are effective means to overcome the potential for subsidence. If excavated soils are to be reused for backfill, they would still be appropriately compacted to mitigate the potential for subsidence or settlement and evaluated for expansion and amended, if necessary, to reduce the potential for expansion in accordance with accepted geotechnical practices.

- Proposed facilities will be designed to include flexible connections, where deemed necessary, along with backfill requirements that minimize the potential for significant damage. All other associated improvements will employ standard design and construction using the most recent geotechnical practices and California Building Code (CBC) seismic criteria, which would provide conservative design criteria.

##### Findings

Based on the EIR/EIS and the entire record before Napa County, the Board finds, in accordance with CEQA Section 15901(a)(1), that changes or alterations have been required in, or incorporated into, the project which avoid or substantially lessen the significant environmental effect as identified in the Final EIR.

##### Rationale

Incorporation of industry standards and materials selection as it applies to the design of the WWTP improvement components and the recycled water conveyance system would comply with AWWA and CBC and would minimize the impact associated with unstable soils.

##### Impact 3.1.4 Expansive Soils

Impact 3.1.4: Project improvements could be located on expansive soils that over time could cause damage to foundations and pipelines resulting in service disruptions.

##### Mitigation

The following mitigation measure is hereby adopted and will be implemented as set forth in the MMRP. This measure will mitigate the above impact to a less-than-significant level.

Mitigation Measure 3.1.1: The Member Agencies will implement the following measures:

- All proposed improvements will be designed and constructed in accordance with current geotechnical industry standard criteria, including the California Building Code (CBC) and American Waterworks Association (AWWA) criteria.

- The project construction materials and backfill materials will be designed according to a geotechnical investigation by a California-licensed geotechnical engineer or engineering geologist to address landslide, subsidence, liquefaction, and expansive soils and seismic hazards such as ground shaking and liquefaction.

- Implementation of industry standard geotechnical measures such as replacing excavated soils with engineered fill materials are effective means to overcome the potential for subsidence. If excavated soils are to be reused for backfill, they would still be appropriately compacted to mitigate the potential for subsidence or settlement and evaluated for expansion and amended, if necessary, to reduce the potential for expansion in accordance with accepted geotechnical practices.

- Proposed facilities will be designed to include flexible connections, where deemed necessary, along with backfill requirements that minimize the potential for significant damage. All other associated improvements will employ standard design and construction using the most recent geotechnical practices and California Building Code (CBC) seismic criteria, which would provide conservative design criteria.

##### Findings

Based on the EIR/EIS and the entire record before Napa County, the Board finds, in accordance with CEQA Section 15901(a)(1), that changes or alterations have been required in, or incorporated into, the project which avoid or substantially lessen the significant environmental effect as identified in the Final EIR.

##### Rationale

Incorporation of industry standards and materials selection as it applies to the design of the WWTP improvement components and the recycled water conveyance system would comply with AWWA and CBC and would reduce the impact related to expansive soils.

#### Section 3.2 Surface Hydrology

##### Impact 3.2.1 Changes in Drainage Patterns

Impact 3.2.1: Project construction could modify existing drainage patterns.

##### Mitigation

The following mitigation measure is hereby adopted and will be implemented as set forth in the MMRP. This measure will mitigate the above impact to a less-than-significant level.

Mitigation Measure 3.2.1: The Member Agencies would implement the following measure during pipeline installation at stream crossings:

- Schedule construction so as to avoid storm events to the extent feasible ;

- Use trenchless techniques such as jack and bore tunneling to avoid direct impacts to the streams;

- Employ short-term drainage diversion and control measures such as sandbags, dikes, pumps, or other means; and

- Following construction, restore the construction area to pre-existing conditions

- Implement Mitigation Measure 3.5.1 (see Section 3.5).

##### Findings

Based on the EIR/EIS and the entire record before Napa County, the Board finds, in accordance with CEQA Section 15901(a)(1), that changes or alterations have been required in, or incorporated into, the project which avoid or substantially lessen the significant environmental effect as identified in the Final EIR.

##### Rationale

As discussed in the Draft EIR/EIS, the proposed pipelines would cross drainages only under certain necessary conditions. In such cases, the measures listed above would avoid direct impact to drainages. The drainage designs would be integrated with existing drainage systems, and the construction site would be restored to pre-existing conditions, therefore, the impact on the drainage patterns would be less than significant.

##### Impact 3.2.3 Increased storm runoff

Impact 3.2.3: New impervious surfaces for the NBWRP would result in an increase in storm runoff.

##### Mitigation

The following mitigation measure is hereby adopted and will be implemented as set forth in the MMRP. This measure will mitigate the above impact to a less-than-significant level.

Mitigation Measure 3.2.3: The Member Agencies will implement the following measures:

- Comply with the local storm drainage requirements;

- Incorporate site design features to control any site runoff onsite; and

- Install storm runoff, collection, and treatment system, as applicable, to control the runoff flow offsite.

##### Findings

Based on the EIR/EIS and the entire record before Napa County, the Board finds, in accordance with CEQA Section 15901(a)(1), that changes or alterations have been required in, or incorporated into, the project which avoid or substantially lessen the significant environmental effect as identified in the Final EIR.

##### Rationale

New impervious surfaces would be added as part of the pump stations located offsite from the WWTPs; however the increase would be minor and compliance with local storm drain requirements and site design features would control runoff flow onsite.

##### Impact 3.2.4	Flooding – Sea Level Rise Impact

Impact 3.2.4: Sea-level rise could affect operation of project facilities.

##### Not Applicable to Napa County.

##### Mitigation Applicable to LGVSD/NMWD, Novato SD/NMWD, SVCSD.

The following mitigation measure is hereby adopted and will be implemented as set forth in the MMRP. This measure will mitigate the above impact to a less-than-significant level.

Mitigation Measure 3.2.4: Design of proposed facilities shall consider sea level rise potential, and shall include appropriate measures in facility siting and design to address potential impacts related to sea level rise, similar to those applied to facility installation within 100-year flood plains. Design measures may include, but are not limited to: facility siting, access placement, access vault extension above projected water elevation, water tight vaults, and site protection.

##### Findings

Based on the Final EIR/EIS and the entire record before Napa County, the Board finds, in accordance with CEQA Section 15901(a)(2) that such changes or alterations are within the responsibility and jurisdiction of another public agency and not the agency making the finding. Such changes have been adopted by such other agency or can and should be adopted by such other agency.

##### Rationale

Based on the Draft EIR/EIS, the proposed project facilities within Napa County jurisdiction would not be located in areas potentially subject to sea-level rise.

#### Section 3.3 Groundwater Resources

##### Impact 3.3.2 Hydrostatic Pressure

Impact 3.3.2: Proposed facilities may be affected by shallow groundwater levels and natural groundwater fluctuations.

##### Mitigation

Mitigation Measure 3.3.1: The Member Agencies will implement the following measures:

- All proposed improvements will be designed and constructed in accordance with current geotechnical industry standard criteria.

- Implement industry standard geotechnical measures to address high groundwater conditions as appropriate to reduce the potential for impacts related to groundwater fluctuation, in accordance with accepted geotechnical practices. Possible design features include drainage blankets, perimeter pumps to temporarily decrease hydrostatic pressure, perimeter drainage trenches, and specific groundwater monitoring scenarios.

##### Findings

Based on the EIR/EIS and the entire record before Napa County, the Board finds, in accordance with CEQA Section 15901(a)(1), that changes or alterations have been required in, or incorporated into, the project which avoid or substantially lessen the significant environmental effect as identified in the Final EIR.

##### Rationale

Proposed facilities, including pipelines, pump stations, and storage facilities would be constructed in accordance with the geotechnical standards and criteria. The design measures would reduce the impacts related to groundwater fluctuation.

#### Section 3.4 Water Quality

##### Impact 3.4.1 Construction-Related Effects

Impact 3.4.1: Disturbance of soils during construction of new project-related infrastructure could generate short term erosion-related water quality impacts. Construction activities could result in the accidental release of fuels or hazardous materials. Project construction activities could require dewatering that could result in the discharge of turbid waters into the local storm drain systems or nearby creeks.

##### Mitigation

The following mitigation measures are hereby adopted and will be implemented as set forth in the MMRP. These measures will mitigate the above impact to a less-than-significant level.

Mitigation Measure 3.4.1a: NPDES Construction Activity Stormwater Permit. Member Agencies or their contractor shall comply with the provisions of the NPDES Construction Activity Stormwater permit, including preparation of Notice of Intent to comply with the provisions of this General Permit and preparation of a Storm Water Pollution Prevention Plan (SWPPP). The SWPPP will identify implementation measures necessary to mitigate potential water quality degradation as a result of construction-related runoff. These measures will include BMPs and other standard pollution prevention actions, such as erosion and sediment control measures, proper control of non-stormwater discharges, and hazardous spill prevention and response. The SWPPP will also include requirements for BMP inspections, monitoring, and maintenance.

The following items are examples of BMPs that would be implemented during construction to avoid causing water quality degradation:

- Erosion control BMPs, such as use of mulches or hydroseeding to prevent detachment of soil, following guidance presented in the California BMP Handbooks – Construction (CASQA 2003). A detailed site map will be included in the SWPPP outlining specific areas where soil disturbance may occur, and drainage patterns associated with excavation and grading activities. In addition, the SWPPP will provide plans and details for the BMPs to be implemented prior, during, and after construction to prevent erosion of exposed soils and to treat sediments before they are transported offsite.

- Sediment control BMPs such as silt fencing or detention basins that trap soil particles.

- Construction staging areas designed so that stormwater runoff during construction will be collected and treated in a detention basin or other appropriate structure.

- Management of hazardous materials and wastes to prevent spills.

- Groundwater treatment BMPs such that localized trench dewatering does not impact surface water quality.

- Vehicle and equipment fueling BMPs such that these activities occur only in designated staging areas with appropriate spill controls.

- Maintenance checks of equipment and vehicles to prevent spills or leaks of liquids of any kind.

##### Findings

Based on the EIR/EIS and the entire record before Napa County, the Board finds, in accordance with CEQA Section 15901(a)(1), that changes or alterations have been required in, or incorporated into, the project which avoid or substantially lessen the significant environmental effect as identified in the Final EIR.

##### Rationale

Implementation of stormwater control measures and BMPs related to handling and storage of hazardous materials would minimize sedimentation and water quality impacts.

##### Impact 3.4.6 Surface Water Storage

Impact 3.4.6: The proposed project would include storage of recycled water at existing WWTP facilities, as well as at individual user properties. Storage of recycled water quality would have the potential to affect localized surface water quality or groundwater quality.

##### Mitigation

The following mitigation measures are hereby adopted and will be implemented as set forth in the MMRP. These measures will mitigate the above impact to a less-than-significant level.

Mitigation Measure 3.4.6a: Under the Master Recycling Permit for each Member Agency and Cooperating Agency, user agreements shall include provisions for compliance with Title 22 and the State Recycled Water Policy regarding storage and use of recycled water onsite at individual properties.

Mitigation Measure 3.4.6b: Prior to storage of recycled water in any “on-stream” storage facility that directly receives and releases stream flow, each Member Agency or Cooperating Agency shall enter into discussions with RWQCB regarding operational requirements to ensure operation of proposed facilities in compliance with Title 22 and the State Recycled Water Policy. It is anticipated that specific operational standards, such as pumping on-stream ponds dry prior to the onset of winter rains or other measures, would be required in order to ensure storage in compliance with Title 22.

##### Findings

Based on the EIR/EIS and the entire record before Napa County, the Board finds, in accordance with CEQA Section 15901(a)(1), that changes or alterations have been required in, or incorporated into, the project which avoid or substantially lessen the significant environmental effect as identified in the Final EIR.

##### Rationale

The project would comply with Title 22 and maintain adequate freeboard to reduce the potential for releases of stored recycled water.

##### Impact 3.4.9 Reuse for Habitat Restoration

Impact 3.4.9: Disinfected tertiary-treated wastewater from the SVCSD and Napa SD WWTPs would be delivered to the Napa Salt Marsh ponds as a dilution source for bittern ponds, thereby improving water quality.

##### Mitigation Not Applicable to Napa County.

Mitigation Not Applicable to LGVSD/NMWD, Novato SD/ NMWD.  

Mitigation Applicable to SVCSD and Napa SD.

Mitigation Measure 3.4.9a: SVCSD and Napa SD (as appropriate) shall implement the following measures:

- Prepare a Management Plan required by the San Francisco Bay RWQCB to obtain a discharge prohibition. The management plan will comply with the RWQCB Resolution 94-086. The management plan will include the following features for Ponds 7 and 7A:

a)	Facility Plan, includes project purpose and objectives, site selection factors, site sampling and analyses, planning and design elements.

b)	Operations and Maintenance plan, includes vegetation planning and harvesting, channel and bank maintenance, pump and gate maintenance, vector controls, and contingency/emergency plans.

c)	Monitoring Program, includes monitoring of pollutants, habitat diversity, wildlife use, and vector populations.

##### Findings

Based on the Final EIR/EIS and the entire record before Napa County, the Board finds, in accordance with CEQA Section 15901(a)(1), that such changes or alterations are within the responsibility and jurisdiction of another public agency and not the agency making the finding. Such changes have been adopted by such other agency or can and should be adopted by such other agency.

##### Rationale

Napa County would not be implementing this component of the project under the Phase 1 Implementation Plan currently under consideration.

#### Section 3.5 Biological Resources

##### Impact 3.5.1 Impacts on Wetlands, Streams and Riparian Habitats

Impact 3.5.1: Construction of the Proposed Project could result in impacts to jurisdictional wetlands and other waters of the United States, as well as impacts to riparian habitat.

##### Mitigation

The following mitigation measure is hereby adopted and will be implemented as set forth in the MMRP. This measure will mitigate the above impact to a less-than-significant level.

Mitigation Measure 3.5.1: Implement the following measures to avoid, minimize and compensate for impacts to jurisdictional wetlands and other waters of the U.S. and impacts to riparian habitat.

Construction activities resulting in the introduction of fill or other disturbance to jurisdictional wetlands and other waters of the U.S. will require permit approval from the U.S. Army Corps of Engineers and water quality certification from the Regional Water Quality Control Board, pursuant to Section 401 of the Clean Water Act. The Proposed Project will most likely be authorized under Nationwide Permit #12 (Utility Lines) pursuant to Section 404 of the Clean Water Act. The California Department of Fish and Game (CDFG) has jurisdiction in the action area over riparian habitat, including stream bed and banks, pursuant to Sections 1600-1616 of the Fish and Game Code. Pipeline construction resulting in alteration to channel bed or banks, extending to the outer dripline of trees forming the riparian corridor, is subject to CDFG jurisdiction. The project proponent will be required to obtain a Streambed Alteration Agreement (SAA) from the CDFG. Terms of these permits and SAA will likely include, but will not necessarily be limited to, the mitigation measures listed below.

    - Specific locations of pipeline segments, storage reservoirs, and pump stations shall be configured, wherever feasible, to avoid and minimize direct and indirect impacts to wetlands and stream drainage channels. Consideration taken in finalizing configuration placement shall include:

- Reducing number and area of stream channel and wetland crossings where feasible. Crossings shall be oriented as close to perpendicular (90 degree angle) to the drainage or wetland as feasible.

- Placement of project components as distant as feasible from channels and wetlands.

- For pipeline construction activities in the vicinity of wetland and stream drainage areas, the construction work area boundaries shall have a minimum 20-foot setback from jurisdictional features. Pipeline construction activities in proximity to jurisdictional features include: 1) entrance and exit pits for directional drilling and bore and jack operations; and 2) portions of pipeline segments listed as “parallel” to wetland/water features.

    - Sites identified as potential staging areas will be examined by a qualified biologist prior to construction. If potentially jurisdictional features are found that could be impacted by staging activities, the site will not be used.

    - Construction methods for channel crossing shall be designed to avoid and minimize direct and indirect impacts to channels to the greatest extent feasible. Use of trenchless methods including suspension of pipeline from existing bridges, directional drilling, and bore and jack tunneling will be used when feasible. Trenchless methods are required for all perennial drainage crossings (i.e., Sonoma Creek). Construction occurring in the vicinity of riparian areas shall be delimited with a minimum 20-foot setback to avoid intrusion of construction activities into sensitive habitat.

The following additional measures shall apply to channel crossings in which the trenching construction method is used:

- Limiting of construction activities in drainage channel crossings to low-flow periods: approximately April 15 to October 15.

- At in-road drainage crossings where drainages pass beneath the road in existing culverts, and where there is sufficient cover between the culvert and road surface, the new pipeline will be installed above the existing culvert without removing or disturbing it. If the pipeline must be installed below the existing culvert, then the culvert will be cut and temporarily removed to allow pipeline installation.

- At off-road drainage crossings, the construction corridor width will be minimized to the greatest extent feasible at the crossing and at least 20 additional feet to either side of the drainage at the crossing.

- If disturbance of the existing culvert is required, sediment curtains upstream and downstream of the construction zone shall be placed to prevent sediment disturbed during trenching activities from being transported and deposited outside of the construction zone.

    - Implement BMPs required in Mitigation Measure 3.4.1 to reduce risk of sediment transport into all construction areas in proximity of drainages.

    - For channels or wetlands for which soil removal is necessary (off-road crossings or wetlands to be trenched or otherwise directly disturbed), the top layer of the drainage or wetland bottom shall be stockpiled and preserved during construction. After the pipeline has been installed, the stockpiled material shall be placed back into the drainage or wetland feature to return the beds to approximately their original composition.

    - To offset temporary and permanent impacts to wetlands and other waters of the U.S., and impacts to riparian habitat, compensatory mitigation will be provided as required by regulatory permits and SAAs.

##### Findings

Based on the EIR/EIS and the entire record before Napa County, the Board finds, in accordance with CEQA Section 15901(a)(1), that changes or alterations have been required in, or incorporated into, the project which avoid or substantially lessen the significant environmental effect as identified in the Final EIR.

##### Rationale

Potential impacts to riparian habitat during construction activities would be reduced by complying with the regulatory requirements and through measures such as avoiding stream crossings as feasible and setting setbacks from sensitive habitats.

##### Impact 3.5.2	Construction Impacts on Special-status Fish and California Freshwater Shrimp

Impact 3.5.2: Construction of Proposed Project facilities could affect special-status invertebrate or fish species including central California coast steelhead, Chinook salmon, California freshwater shrimp, Pacific lamprey, and Sacramento splittail, or designated critical habitat for steelhead.

##### Mitigation

The following mitigation measure is hereby adopted and will be implemented as set forth in the MMRP. This measure will mitigate the above impact to a less-than-significant level.

Mitigation Measure 3.5.2: Specific measures shall be implemented to protect aquatic habitats potentially inhabited by special-status fish and California freshwater shrimp.

Sensitive fisheries and other aquatic resources shall be protected by minimizing in-stream and near-stream habitat impacts during project design, informally consulting with resource agencies (NMFS, USFWS, CDFG, and USACOE), and implementing protective measures. For Sonoma Creek, Petaluma River, Napa River, and other perennial drainages, special-status fish are presumed present. California freshwater shrimp are presumed present in Sonoma Creek. Because of the sensitivity of seasonal and ephemeral drainages, the following measures will be required to avoid and minimize impacts to aquatic habitat:

- Project designs shall be reconfigured, whenever feasible, to avoid direct impacts to sensitive wetland areas and minimize disturbances to wetland and riparian corridors. Ground disturbance and construction footprints in these areas shall be minimized to the greatest degree feasible.

- If trenching or directional boring stream crossing methods are used, the construction schedule of such activities shall be implemented according to conditions of the SAAs.

- In-stream construction shall be avoided at all locations that are known, or presumed, to support threatened or endangered species, if at the time of construction such locations contain flowing or standing water.

- In the event that equipment shall operate in any watercourse with flowing or standing water, the project proponent will ensure that they have the appropriate permit authorizations.

- Prior to construction, a qualified biologist shall install fencing to establish a minimum 20-foot setback from sensitive habitat.

- For work sites located adjacent to sensitive aquatic sites, a biological resource education program shall be provided by a qualified biologist, as per conditions of the SAAs.

##### Findings

Based on the EIR/EIS and the entire record before Napa County, the Board finds, in accordance with CEQA Section 15901(a)(1), that changes or alterations have been required in, or incorporated into, the project which avoid or substantially lessen the significant environmental effect as identified in the Final EIR.

##### Rationale

The project would be designed to avoid sensitive wetland areas and measures such as educating the construction workers would minimize the impacts to special-status species.

##### Impact 3.5.4 Impacts on Special-status Invertebrates

Impact 3.5.4: Construction of Proposed Project facilities could impact special-status invertebrates including Myrtle’s silverspot butterfly, Opler’s longhorn moth, Monarch butterfly wintering sites, Ricksecker’s water scavenger beetle and California brackish water snail.

##### Mitigation

The following mitigation measure is hereby adopted and will be implemented as set forth in the MMRP. This measure will mitigate the above impact to a less-than-significant level.

Mitigation Measure 3.5.3: Implementation of Mitigation Measure 3.5.5 for the protection of California red-legged frogs and Mitigation Measure 3.5.1 for protection and restoration of wetlands would protect special-status invertebrates that could potentially be impacted by the project. No specific mitigation is required.

##### Findings

Based on the EIR/EIS and the entire record before Napa County, the Board finds, in accordance with CEQA Section 15901(a)(1), that changes or alterations have been required in, or incorporated into, the project which avoid or substantially lessen the significant environmental effect as identified in the Final EIR.

##### Rationale

Implementation of measures to protect the California red-legged frog and wetlands would also minimize impacts to special-status invertebrates.

##### Impact 3.5.5 Impacts on Western Pond Turtle

Impact 3.5.5: Construction of the proposed project has the potential to impact western pond turtles in upland and aquatic habitat.

##### Mitigation

The following mitigation measure is hereby adopted and will be implemented as set forth in the MMRP. This measure will mitigate the above impact to a less-than-significant level.

Mitigation Measure 3.5.5: The appropriate Member Agency shall implement protection measures to avoid and minimize impacts to western pond turtles.

- When working within 200 feet of stream crossings, all construction personnel shall receive awareness training relating to the protection of western pond turtles, in accordance with the SAAs. Also, to minimize the likelihood of encountering turtles in upland areas near stream crossings, construction footprints shall be minimized to the greatest extent feasible. Based on reconnaissance-level surveys, if staging and construction activities occur principally within or immediately adjacent to project alignment roads the project will be outside of principal pond turtle habitat.

- Within 48 hours prior to the start of construction activities, a qualified biologist shall perform pond turtle surveys within suitable habitat within projected work areas. If a pond turtle nest is located within a work area, a biologist with the appropriate permits may move the eggs to a suitable facility for incubation, and release hatchlings into the creek system in late fall.

The measures proposed for protection of aquatic species and red-legged frogs (Mitigation Measures 3.5.2 and 3.5.6) will additionally protect western pond turtles during construction.

##### Findings

Based on the EIR/EIS and the entire record before Napa County, the Board finds, in accordance with CEQA Section 15901(a)(1), that changes or alterations have been required in, or incorporated into, the project which avoid or substantially lessen the significant environmental effect as identified in the Final EIR.

##### Rationale

Measures such as conducting surveys for pond turtles prior to construction and establishing working areas at a specified distance from the stream crossings would minimize the impact.

##### Impact 3.5.6 Impacts on California Red-legged Frog

Impact 3.5.6: Construction of the Proposed Project has the potential to affect California red-legged frogs, if present.

##### Mitigation

The following mitigation measure is hereby adopted and will be implemented as set forth in the MMRP. This measure will mitigate the above impact to a less-than-significant level.

Mitigation Measure 3.5.6: The appropriate Member Agency shall implement the following protection measures to avoid and minimize impacts on California red-legged frog.

- The implementation of measures identified for the protection of special-status fish and California freshwater shrimp would also protect California red-legged frogs within aquatic habitat. All protection measures identified in Mitigation Measure 3.5.2 shall be applied to the protection of red-legged frogs at sites that provide potential aquatic habitat for this species. These include informal USFWS consultation, avoiding aquatic habitat, establishing a suitable buffer from the aquatic habitat (e.g., 50 feet), and implementing a worker education program.

- All work activities within or adjacent to aquatic habitat that is potentially occupied by red-legged frogs will be completed between May 1 and November 1.

- A qualified biological resource monitor will conduct a training session for construction personnel working in upland habitat near potentially occupied drainages, as per conditions of the SAAs.

- All trash that could attract predators will be regularly contained and removed from the work site.

In the event trenchless methods cannot be employed, the project proponent would obtain appropriate permit authorizations and implement construction methods per applicable Streambed Alteration Agreements.

##### Findings

Based on the EIR/EIS and the entire record before Napa County, the Board finds, in accordance with CEQA Section 15901(a)(1), that changes or alterations have been required in, or incorporated into, the project which avoid or substantially lessen the significant environmental effect as identified in the Final EIR.

##### Rationale

Measures for protecting special-status fish and freshwater shrimp would apply to the protection of California red-legged frog. Mitigation including informal USFWS consultation, avoiding aquatic habitat, and establishing a suitable buffer would minimize the impact.

##### Impact 3.5.7 Impacts on Threatened and Endangered Marsh Birds

Impact 3.5.7: Construction of the proposed project has the potential to affect western snowy plover, California black rail and California clapper rail and their habitat in and near the project alignments.

##### Mitigation

The following mitigation measure is hereby adopted and will be implemented as set forth in the MMRP. This measure will mitigate the above impact to a less-than-significant level.

Mitigation Measure 3.5.7: Impacts to Threatened and Endangered Marsh Birds. To minimize the likelihood of project effects on threatened and endangered marsh birds, the following reasonable and prudent measures would be implemented by the appropriate Member Agency:

- Protocol-level surveys will be conducted in locations with suitable habitat to determine species presence or absence.

- Agency consultation will be initiated.

- Construction activities will occur during the non-breeding season, September 15 through January 31. The combined breeding season for all three species extends from February 1 through September 14.

- Construction personnel will receive environmental awareness training specific to the identification of clapper rails, black rails, western snowy plover and their habitat.

- Any clapper rail and western snowy plover activity will be immediately reported to the USFWS; black rail activity will be reported to the CDFG.

- Construction activities will be constrained to the smallest area possible to minimize marsh disturbance.

##### Findings

Based on the EIR/EIS and the entire record before Napa County, the Board finds, in accordance with CEQA Section 15901(a)(1), that changes or alterations have been required in, or incorporated into, the project which avoid or substantially lessen the significant environmental effect as identified in the Final EIR.

##### Rationale

Measures such as conducting surveys for threatened and endangered marsh birds prior to construction and restricting construction activities to non-breeding season would minimize the impact.

##### Impact 3.5.8 Impacts on Burrowing Owl

Impact 3.5.8: Construction of the proposed project could result in direct and indirect impacts to burrowing owls, if present in portions of the project alignment. (Less than Significant with Mitigation)

##### Mitigation

The following mitigation measure is hereby adopted and will be implemented as set forth in the MMRP. This measure will mitigate the above impact to a less-than-significant level.

Mitigation Measure 3.5.8: The following measures to avoid, minimize, or mitigate impacts on burrowing owls would be incorporated into the project by the appropriate Member Agency:

- In areas identified to provide potential burrowing owl habitat, preconstruction surveys for burrowing owls would be conducted by a qualified biologist 14-30 days prior to the start of construction. Surveys would cover grassland areas within 500-foot buffer and check for adult and juvenile burrowing owls and their habitat.

- Construction exclusion areas would be established around the occupied burrows in which no disturbance would be allowed to occur. During the non-breeding season (September 1 through January 31), the exclusion zone would extend 160 feet around occupied burrows. During the breeding season (February 1 through August 31), exclusion areas would extend 250 feet around occupied burrows. Passive relocation of owls is not proposed.

- A qualified biologist (the on-site monitor or otherwise) will monitor owl activity on the site to ensure the species is not adversely affected by the project.

##### Findings

Based on the EIR/EIS and the entire record before Napa County, the Board finds, in accordance with CEQA Section 15901(a)(1), that changes or alterations have been required in, or incorporated into, the project which avoid or substantially lessen the significant environmental effect as identified in the Final EIR.

##### Rationale

Measures such as conducting surveys for burrowing owl prior to construction and restricting construction activities to non-breeding season would minimize the impact.

##### Impact 3.5.9 Impacts on Nesting Birds

Impact 3.5.9: Construction of the proposed project has the potential to affect nesting birds including Swainson’s hawk, willow flycatcher, sharp-shinned hawk, Cooper’s hawk, tri-colored blackbird, Bell’s sage sparrow, golden eagle, northern harrier, California yellow-warbler, white-tailed kite, California horned lark, salt marsh common yellowthroat, loggerhead shrike, San Pablo song sparrow, California thrasher, rookeries, and additional bird species protected by California Fish and Game Code Section 3503 and the federal Migratory Bird Treaty Act (16 USC, Sec. 703, Supp. I, 1989). (Less than Significant with Mitigation)

##### Mitigation

The following mitigation measure is hereby adopted and will be implemented as set forth in the MMRP. This measure will mitigate the above impact to a less-than-significant level.

Mitigation Measure 3.5.9: To avoid disturbing common and special-status nesting birds, the following protection measures shall be implemented:

- Whenever feasible, vegetation shall be removed during the non-breeding season (generally defined as September 1 to January 31).

- For ground disturbing activities occurring during the breeding season (generally defined as February 1 to August 31), a qualified wildlife biologist will conduct preconstruction surveys of all potential nesting habitat for birds within 500 feet of earthmoving activities.

- If active bird nests are found during preconstruction surveys, a 500-foot no-disturbance buffer will be created around active raptor nests during the breeding season or until it is determined that all young have fledged. A 250-foot buffer zone will be created around the nests of other special-status birds. These buffer zones are consistent with CDFG avoidance guidelines; however, they may be modified in coordination with CDFG based on existing conditions at work locations.

- If preconstruction surveys indicate that nests are inactive or potential habitat is unoccupied during the construction period, no further mitigation is required. Trees and shrubs that have been determined to be unoccupied by special-status birds or that are located at least 500 feet from active nests may be removed.

##### Findings

Based on the EIR/EIS and the entire record before Napa County, the Board finds, in accordance with CEQA Section 15901(a)(1), that changes or alterations have been required in, or incorporated into, the project which avoid or substantially lessen the significant environmental effect as identified in the Final EIR.

##### Rationale

Measures such as conducting surveys for nesting birds prior to construction and restricting construction activities to non-breeding season would minimize the impact.

##### Impact 3.5.10	Impacts on Salt Marsh Harvest Mouse and Suisun Ornate Shrew

Impact 3.5.10: Construction of the proposed project has the potential to affect salt marsh harvest mouse and suisun ornate shrew and their habitat in and near the project alignments.

##### Mitigation

The following mitigation measure is hereby adopted and will be implemented as set forth in the MMRP. This measure will mitigate the above impact to a less-than-significant level.

Mitigation Measure 3.5.10: The appropriate Member Agency shall implement protection measures to avoid and minimize impacts on salt marsh mammals during construction.

Where avoidance of sensitive habitat is not feasible (e.g., by bridging or bore and jack), consultation with CDFG and/or USFWS would be initiated. If species are present or presumed to be present after informal consultation with USFWS and/or CDFG, then a formal consultation and Biological Assessment in support of a Biological Opinion would be required. Such a consultation would proceed as part of the Corps 404 permitting program.

To avoid potential impacts on salt marsh harvest mouse and Suisun ornate shrew, a qualified biologist shall conduct specific preconstruction surveys prior to project initiation, following USFWS survey guidelines. The project proponent shall install exclusionary fences to prevent species movement into the action area, and a biologist with the appropriate permits to relocate these species shall live-trap mice and shrews within the enclosure and move these animals outside the fence. The biological monitor shall inspect these fences to ensure their integrity, and shall conduct an education workshop for contractors employees outlining species’ biology, legislative protection, and construction restrictions to reduce potential impacts.

##### Findings

Based on the EIR/EIS and the entire record before Napa County, the Board finds, in accordance with CEQA Section 15901(a)(1), that changes or alterations have been required in, or incorporated into, the project which avoid or substantially lessen the significant environmental effect as identified in the Final EIR.

##### Rationale

Measures such as conducting surveys for salt harvest mouse and Suisun ornate shrew prior to construction and restricting construction activities to non-breeding season would minimize the impact.

##### Impact 3.5.11	Impacts on Special Status Bats

Impact 3.5.11: Construction of the proposed project has the potential to affect roosting or breeding special-status bats in and near the project alignments.

##### Mitigation

The following mitigation measure is hereby adopted and will be implemented as set forth in the MMRP. This measure will mitigate the above impact to a less-than-significant level.

Mitigation Measure 3.5.11: The appropriate Member Agency shall implement protection measures to avoid and minimize impacts on special-status bats in and near project facilities during construction.

Concurrent with breeding bird surveys (Mitigation Measure 3.5.8), a qualified biologist will conduct preconstruction surveys for special-status bats at each bridge crossing location and in rural (i.e., non-road) areas where any large trees (e.g., > 24 inch diameter at breast height) will be removed. If an active roost is observed, a suitably-sized buffer (e.g., 100 to 150 feet) will be placed around the roost if it appears that trenching or other project activities may cause abandonment. Demolition activities must cease until juvenile bats are self-sufficient and will not be directly or indirectly impacted by activities.

##### Findings

Based on the EIR/EIS and the entire record before Napa County, the Board finds, in accordance with CEQA Section 15901(a)(1), that changes or alterations have been required in, or incorporated into, the project which avoid or substantially lessen the significant environmental effect as identified in the Final EIR.

##### Rationale

Measures such as conducting pre-construction surveys for special-status bats and avoiding or maintaining a suitable buffer from an active roost would minimize the impact.

##### Impact 3.5.12 Impacts on American Badger

Impact 3.5.12: Construction of the proposed project has the potential to affect American badger and its habitat in and near the project alignments.

##### Mitigation

The following mitigation measure is hereby adopted and will be implemented as set forth in the MMRP. This measure will mitigate the above impact to a less-than-significant level.

Mitigation Measure 3.5.12: To avoid and minimize impacts on badgers, the appropriate Member Agency shall implement preconstruction surveys prior to ground clearing and grading in annual grasslands habitat or areas that are known or suspected to support badger.

- Within 30-days prior to ground-clearing, a qualified biologist shall survey areas that provide potential badger habitat that occur within 100-feet of project activities. If no evidence of badgers presence is detected, no further mitigation is required. If active badger dens are identified within the action area, badgers will be passively relocated. If identified, vacated dens shall be temporarily covered using plywood sheets or similar materials to prevent badgers from returning to the action area during construction.

##### Findings

Based on the EIR/EIS and the entire record before Napa County, the Board finds, in accordance with CEQA Section 15901(a)(1), that changes or alterations have been required in, or incorporated into, the project which avoid or substantially lessen the significant environmental effect as identified in the Final EIR.

##### Rationale

Measures such as conducting pre-construction surveys for American badger and temporary covers on vacated dens would avoid or minimize the impact.

##### Impact 3.5.13 Impacts on Rare Plants

Impact 3.5.13: Project construction could result in impacts to listed and other special-status plants.

##### Mitigation

The following mitigation measure is hereby adopted and will be implemented as set forth in the MMRP. This measure will mitigate the above impact to a less-than-significant level.

Mitigation Measure 3.5.13. Before the initiation of any vegetation removal or ground-disturbing activities in areas that provide suitable habitat for special-status plants, the following measures shall be implemented by the appropriate Member Agency:

- A qualified botanist will conduct appropriately-timed surveys for special-status plant species, including those identified in Table 3.5.1, in all suitable habitat that would be potentially disturbed by the project.

- Surveys shall be conducted following CDFG- or other approved protocol.

- If no special-status plants are found during focused surveys, the botanist shall document the findings in a letter to the appropriate agencies and no further mitigation will be required.

If special-status plants are found during focused surveys, the following measures shall be implemented:

  - Information regarding the special-status plant population shall be reported to the California Natural Diversity Database (CNDDB).

  - If the populations can be avoided during project implementation, they shall be clearly marked in the field by a qualified botanist and avoided during construction activities. Before ground clearing or ground disturbance, all on-site construction personnel shall be instructed as to the species’ presence and the importance of avoiding impacts to this species and its habitat.

  - If special-status plant populations cannot be avoided, consultations with CDFG and/or USFWS would be required. A plan to compensate for the loss of special-status plant species could be required, detailing appropriate replacement ratios, methods for implementation, success criteria, monitoring and reporting protocols, and contingency measures that would be implemented if the initial mitigation fails; the plan would be developed in consultation with the appropriate agencies prior to the start of local construction activities.

  - If mitigation is required, the project proponent shall maintain and monitor the mitigation area for 5 years following the completion of construction and restoration activities. Monitoring reports shall be submitted to the resource agencies at the completion of restoration and for 5 years following restoration implementation. Monitoring reports shall include photo-documentation, planting specifications, a site layout map, descriptions of materials used, and justification for any deviations from the mitigation plan.

##### Findings

Based on the EIR/EIS and the entire record before Napa County, the Board finds, in accordance with CEQA Section 15901(a)(1), that changes or alterations have been required in, or incorporated into, the project which avoid or substantially lessen the significant environmental effect as identified in the Final EIR.

##### Rationale

Measures such as conducting surveys of vegetation and consultation with USFWS and CDFG as required, would minimize the impact.

##### Impact 3.5.14 Impacts on Heritage and Significant Trees

Impact 3.5.14: The proposed project could affect heritage and other significant trees.

##### Mitigation

The following mitigation measure is hereby adopted and will be implemented as set forth in the MMRP. This measure will mitigate the above impact to a less-than-significant level.

Mitigation Measure 3.5.14: The following measures shall be implemented by the appropriate Member Agency to avoid or reduce impacts to heritage or other significant trees:

- Prior to the commencement of construction activities, trees necessary to remove or at risk of being damaged will be identified.

- A certified arborist will inventory these trees, with the results of the inventory providing species, size (diameter at breast height, or dbh), and number of protected trees. Also, in consultation with the appropriate County, the arborist will determine if any are heritage or landmark trees.

- If any protected trees are identified that will be potentially removed or damaged by construction of the proposed project, design changes will be implemented where feasible to avoid the impact.

- Any protected trees that are removed will be replaced per applicable City and County tree protection ordinances. Foliage protectors (cages and tree shelters) will be installed to protect the planted trees from wildlife browse. The planted trees will be monitored as required by the ordinance, or regularly during a minimum two-year establishment period and maintenance during the plant establishment period will include irrigation. After the establishment period, the native tree plantings are typically capable of survival and growth without supplemental irrigation.

##### Findings

Based on the EIR/EIS and the entire record before Napa County, the Board finds, in accordance with CEQA Section 15901(a)(1), that changes or alterations have been required in, or incorporated into, the project which avoid or substantially lessen the significant environmental effect as identified in the Final EIR.

##### Rationale

Measures such as avoiding protected trees and replacing any removing trees as per the local tree protection ordinances would minimize the impact to heritage and significant trees.

#### Section 3.6 Land Use

##### Impact 3.6.3 Impact to Farmland

Impact 3.6.3: Construction activities associated with the project could temporarily affect the agricultural use of important farmland.

##### Mitigation

The following mitigation measure is hereby adopted and will be implemented as set forth in the MMRP. This measure will mitigate the above impact to a less-than-significant level.

Mitigation Measure 3.6.1: To support the continued productive use of Important Farmlands in the action area, the appropriate Member Agency shall implement the following measures during project construction:

- Replace soils over pipelines in a manner that will minimize any negative impacts on crop productivity. The surface and subsurface soil layers will be stockpiled separately and returned to their appropriate locations in the soil profile.

- To avoid over-compaction of the top layers of soil, monitor pre-construction soil densities and return the surface soil (approximately the top 3 feet) to within 5 percent of original density.

- Where necessary, rip the top soil layers to achieve the appropriate soil density. Ripping may also be used in areas where vehicle and equipment traffic have compacted the top soil layers, such as the construction staging areas.

- Avoid working or traveling on wet soil to minimize compaction and loss of soil structure. Before construction begins, geotechnical testing will be done to determine the moisture content limit above which work should not occur. Where working or driving on wet soil cannot be avoided, roadways will be capped with spoils that will be removed at the end of construction and/or ripped and amended with organic material as needed.

- Remove all construction-related debris from the soil surface. This will prevent rock, gravel, and construction debris from interfering with agricultural activities.

- Perform soil density monitoring during backfill and ripping to minimize excessive compaction and minimize effects on future agricultural land use.

- Remove topsoil before excavating in fields. Return it to top of fields to avoid detrimental inversion of soil profiles.

- Control compaction to minimize changes to lateral groundwater flow which could affect both irrigation and internal drainage.

##### Findings

Based on the EIR/EIS and the entire record before Napa County, the Board finds, in accordance with CEQA Section 15901(a)(1), that changes or alterations have been required in, or incorporated into, the project which avoid or substantially lessen the significant environmental effect as identified in the Final EIR.

##### Rationale

Measures to support the continued productive use of important farmlands in the action area would mitigate any impacts from project construction.

##### Impact 3.6.4 Conversion of Farmland

Impact 3.6.4: The project would permanently convert Important Farmland to nonagricultural use.

##### Mitigation

The following mitigation measure is hereby adopted and will be implemented as set forth in the MMRP. This measure will mitigate the above impact to a less-than-significant level.

Mitigation Measure 3.6.4: To support the continued productive use of Important Farmlands in the action area, the appropriate Member Agency shall implement the following measures during project construction:

- Replace soils over pipelines in a manner that will minimize any negative impacts on crop productivity. The surface and subsurface soil layers will be stockpiled separately and returned to their appropriate locations in the soil profile.

- To avoid over-compaction of the top layers of soil, monitor pre-construction soil densities and return the surface soil (approximately the top 3 feet) to within 5 percent of original density.

- Where necessary, rip the top soil layers to achieve the appropriate soil density. Ripping may also be used in areas where vehicle and equipment traffic have compacted the top soil layers, such as the construction staging areas.

- Avoid working or traveling on wet soil to minimize compaction and loss of soil structure. Before construction begins, geotechnical testing will be done to determine the moisture content limit above which work should not occur. Where working or driving on wet soil cannot be avoided, roadways will be capped with spoils that will be removed at the end of construction and/or ripped and amended with organic material as needed.

- Remove all construction-related debris from the soil surface. This will prevent rock, gravel, and construction debris from interfering with agricultural activities.

- Perform soil density monitoring during backfill and ripping to minimize excessive compaction and minimize effects on future agricultural land use.

- Remove topsoil before excavating in fields. Return it to top of fields to avoid detrimental inversion of soil profiles.

- Control compaction to minimize changes to lateral groundwater flow which could affect both irrigation and internal drainage.

##### Findings

Based on the EIR/EIS and the entire record before Napa County, the Board finds, in accordance with CEQA Section 15901(a)(1), that changes or alterations have been required in, or incorporated into, the project which avoid or substantially lessen the significant environmental effect as identified in the Final EIR.

##### Rationale

Based on the Final EIR/EIS and the entire record before Napa County, the Board finds that the mitigation measure will reduce the significant effect to a less-than-significant level.

#### Section 3.7 Traffic and Transportation

##### Impact 3.7.1 Temporary Congestion and Delays

Impact 3.7.1: Project construction activities could adversely affect traffic and transportation conditions in the action area.

##### Mitigation

The following mitigation measures are hereby adopted and will be implemented as set forth in the MMRP. The measures will mitigate the above impact to a less-than-significant level.

Mitigation Measure 3.7.1a: The appropriate Member Agency for each project component shall obtain and comply with local road encroachment permits for roads that are affected by construction activities.

The Work Area Protection and Traffic Control Manual includes requirements to ensure safe maintenance of traffic flow through or around the construction work zone, and safe access of police, fire, and other rescue vehicles (CJUTCC, 1996). In addition, the Traffic Management Plan (subject to local jurisdiction review and approval) required by Mitigation Measure 3.7.1b, below, would direct how traffic flow is safely maintained during project construction.

Mitigation Measure 3.7.1b: The construction contractor for each project component shall prepare and implement a Traffic Control/Traffic Management Plan subject to approval by the appropriate local jurisdiction prior to construction. The plan shall:

Identify hours of construction (between 8:00 AM and 7:00 PM; no construction shall be permitted between 10:00 PM and 7:00 AM);

Identify hours for deliveries (Monday – Friday, 9:00 AM to 3:30 PM, or other hours if approved by the appropriate local jurisdiction);

Include a discussion of haul routes, limits on the length of open trench, work area delineation, traffic control and flagging;

Identify all access and parking restriction, pavement markings and signage requirements (e.g., speed limit, temporary loading zones);

Layout a plan for notifications and a process for communication with affected residents and businesses prior to the start of construction. Advance public notification shall include posting of notices and appropriate signage of construction activities. The written notification shall include the construction schedule, the exact location and duration of activities within each street (i.e., which lanes and access point/driveways would be blocked on which days and for how long), and a toll-free telephone number for receiving questions or complaints;

Include a plan to coordinate all construction activities with emergency service providers in the area at least one month in advance. Emergency service providers shall be notified of the timing, location, and duration of construction activities. All roads shall remain passable to emergency service vehicles at all times;

Include a plan to coordinate all construction activities with the appropriate local school district at least two months in advance. The school district shall be notified of the timing, location, and duration of construction activities. Coordinate with the appropriate local school district to identify peak circulation periods at schools along the alignment(s) (i.e., the arrival and departure of students), and require their contractor to avoid construction and lane closures during those periods. The construction contractor for each project component shall be required to maintain vehicle, pedestrian, and school bus service during construction through inclusion of such provisions in the construction contract. The assignment of temporary crossing guards at designated intersections may be needed to enhance pedestrian safety during project construction;

Include the requirement that all open trenches be covered with metal plates at the end of each workday to accommodate traffic and access; and

Specify the street restoration requirements pursuant to agreements with the local jurisdictions.

Mitigation Measure 3.7.1c: The appropriate Member Agency for each project component shall identify all roadway locations where special construction techniques (e.g., horizontal boring, directional drilling or night construction) will be used to minimize impacts to traffic flow.

Mitigation Measure 3.7.1d: The appropriate Member Agency for each project component shall develop circulation and detour plans to minimize impact to local street circulation. This may include the use of signing and flagging to guide vehicles through and/or around the construction zone.

Mitigation Measure 3.7.1e: The appropriate Member Agency for each project component shall encourage construction crews to park at staging areas to limit lane closures in the public right-of-way.

Mitigation Measure 3.7.1f: The appropriate Member Agency for each project component shall consult with the appropriate public transit service providers at least one month prior to construction to coordinate bus stop relocations (as necessary) and to reduce potential interruption of transit service.

##### Findings

Based on the EIR/EIS and the entire record before Napa County, the Board finds, in accordance with CEQA Section 15901(a)(1), that changes or alterations have been required in, or incorporated into, the project which avoid or substantially lessen the significant environmental effect as identified in the Final EIR.

##### Rationale

Traffic mitigating measures such as preparing an implementing a traffic control and management plan and complying with the local road encroachment permits would minimize impacts from congestion during project construction.

##### Impact 3.7.2 Temporary Disruption to Access

Impact 3.7.2: Project construction activity would temporarily disrupt circulation patterns near sensitive land uses (schools, hospitals, fire stations, police stations, and other emergency providers).

##### Mitigation

Mitigation Measure 3.7.2a: Pipeline construction near schools shall occur when school is not in session (i.e., summer or holiday breaks). If this is not feasible, a minimum of two months prior to project construction, the appropriate Member Agency for each project component shall coordinate with the appropriate local school district to identify peak circulation periods at schools along the alignment(s) (i.e., the arrival and departure of students), and require their contractor to avoid construction and lane closures during those periods.

Mitigation Measure 3.7.2b: A minimum of two months prior to project construction, the appropriate Member Agency for each project component shall coordinate with the appropriate local school district to identify alternatives to their Safe Routes to School program, alternatives for the school busing routes and stop locations, and other circulation provisions, as part of the Traffic Control/Traffic Management Plan (see Mitigation Measure 3.7.1a).

Mitigation Measure 3.7.2c: Implement Mitigation Measure 3.7.1b.

##### Findings

Based on the EIR/EIS and the entire record before Napa County, the Board finds, in accordance with CEQA Section 15901(a)(1), that changes or alterations have been required in, or incorporated into, the project which avoid or substantially lessen the significant environmental effect as identified in the Final EIR.

##### Rationale

Coordination with local school districts and identifying alternative traffic routes would minimize the impacts from temporary disruption to access to sensitive land uses.

##### Impact 3.7.3 Temporary Disruption to Access

Impact 3.7.3: Project construction activity would have temporary effects on alternative transportation or alternative transportation facilities.

##### Mitigation

The following mitigation measure is hereby adopted and will be implemented as set forth in the MMRP. The measure will mitigate the above impact to a less-than-significant level.

Mitigation Measure 3.7.3: Implement Mitigation Measure 3.7.1f.

##### Findings

Based on the EIR/EIS and the entire record before Napa County, the Board finds, in accordance with CEQA Section 15901(a)(1), that changes or alterations have been required in, or incorporated into, the project which avoid or substantially lessen the significant environmental effect as identified in the Final EIR.

##### Rationale

Consulting with the appropriate public transit service providers prior to construction would minimize effects on access to alternative transportation facilities.

##### Impact 3.7.4 Temporary Displacement of Parking

Impact 3.7.4: Project construction activity would temporarily create parking demand for construction workers and construction vehicles, and displace parking spaces.

##### Mitigation

The following mitigation measure is hereby adopted and will be implemented as set forth in the MMRP. The measure will mitigate the above impact to a less-than-significant level.

Mitigation Measure 3.7.4: Implement Mitigation Measure 3.7.1e.

##### Findings

Based on the EIR/EIS and the entire record before Napa County, the Board finds, in accordance with CEQA Section 15901(a)(1), that changes or alterations have been required in, or incorporated into, the project which avoid or substantially lessen the significant environmental effect as identified in the Final EIR.

##### Rationale

Parking at construction staging areas would reduce the impacts from the increase in parking demand for construction workers.

##### Impact 3.7.5 Temporary Potential Traffic Hazards

Impact 3.7.5: Project construction activity would temporarily increase the potential for accidents on project roadways.

##### Mitigation

The following mitigation measure is hereby adopted and will be implemented as set forth in the MMRP. The measure will mitigate the above impact to a less-than-significant level.

Mitigation Measure 3.7.5: Implement Mitigation Measure 3.7.1b through 3.7.1f.

##### Findings

Based on the EIR/EIS and the entire record before Napa County, the Board finds, in accordance with CEQA Section 15901(a)(1), that changes or alterations have been required in, or incorporated into, the project which avoid or substantially lessen the significant environmental effect as identified in the Final EIR.

##### Rationale

Measures noted above to reduce traffic congestion and delays from increased traffic from project construction would minimize any related traffic hazards.

##### Impact 3.7.6 Road Wear

Impact 3.7.6: Project construction activity would increase wear and tear on the designated haul routes used by construction vehicles to access the project work sites.

##### Mitigation

The following mitigation measure is hereby adopted and will be implemented as set forth in the MMRP. The measure will mitigate the above impact to a less-than-significant level.

Mitigation Measure 3.7.6: Roads damaged by construction shall be repaired to a structural condition equal to that which existed prior to construction activity as per conditions of the encroachment permit (see Mitigation Measure 3.7.1a).

##### Findings

Based on the EIR/EIS and the entire record before Napa County, the Board finds, in accordance with CEQA Section 15901(a)(1), that changes or alterations have been required in, or incorporated into, the project which avoid or substantially lessen the significant environmental effect as identified in the Final EIR.

##### Rationale

The roads used for construction would be restored to pre-existing condition, therefore the traffic from project construction would not cause significant road wear.

#### Section 3.8 Air Quality

##### Impact 3.8.1 Temporary Construction Emission of Criteria Pollutants

Impact 3.8.1: Project construction activities could result in substantial short-term criteria pollutant emissions.

##### Mitigation

The following mitigation measures are hereby adopted and will be implemented as set forth in the MMRP. The measures will mitigate the above impact to a less than significant level.

Mitigation Measure 3.8.1a: Construction Fugitive Dust Control Plan. The appropriate Member Agency shall require its contractor(s) to implement a dust control plan that shall include the following dust control procedures during construction as required by the BAAQMD:

- Water all active construction areas at least twice daily, taking into consideration temperature and wind conditions.

- Cover all trucks hauling soil, sand, and other loose materials or require trucks to maintain at least two feet of freeboard.

- Pave, apply water three times daily, or apply (non-toxic) soil stabilizers on unpaved access roads, parking areas and staging areas at construction sites.

- Sweep daily (with water sweepers) all paved access roads, parking areas and staging areas at construction sites.

- Sweep streets daily (with water sweepers) if visible soil material is carried onto adjacent public streets.

- Hydroseed or apply (non-toxic) soil stabilizers to inactive construction areas (previously graded areas inactive for ten days or more).

- Enclose, cover, water twice daily or apply (non-toxic) soil binders to exposed stockpiles (dirt, sand, etc.)

- Limit traffic speeds on unpaved roads to 15 mph.

- Install sandbags or other erosion control measures to prevent silt runoff to public roadways, consistent with Mitigation Measure 3.1.2, Erosion Control.

- Replant vegetation in disturbed areas as quickly as possible.

Mitigation Measure 3.8.1b: Construction Exhaust Emissions Control Plan. The appropriate Member Agency shall require its contractor(s) to implement an exhaust emissions control plan that shall include the following controls and practices:

- On road vehicles with a gross vehicular weight rating of 10,000 pounds or greater shall not idle for longer than five minutes at any location as required by Section 2485 of Title 13, Division 3, Chapter 10, Article 1 of the California Code of Regulations. This restriction does not apply when vehicles remain motionless during traffic or when vehicles are queuing.

- Off road equipment engines shall not idle for longer than five minutes per Section 2449(d)(3) of Title 13, Division 3, Chapter 9, Article 4.8 of the California Code of Regulations. All vehicle operators shall receive a written idling policy to inform them of idling restrictions. The policy shall list exceptions to this rule that include the following: idling when queuing; idling to verify that the vehicle is in safe operating condition; idling for testing, servicing, repairing or diagnostic purposes; idling necessary to accomplish work for which the vehicle was designed (such as operating a crane); idling required to bring the machine to operating temperature as specified by the manufacturer; and idling necessary to ensure safe operation of the vehicle.

- Off road engines greater than 50 horsepower shall, at a minimum, meet Tier 2 emissions standards. When available, higher Tier engines shall be utilized. Additionally, contractor(s) shall comply with current CARB and BAAQMD regulations for off-road engines greater than 50 horsepower.

##### Findings

Based on the EIR/EIS and the entire record before Napa County, the Board finds, in accordance with CEQA Section 15901(a)(1), that changes or alterations have been required in, or incorporated into, the project which avoid or substantially lessen the significant environmental effect as identified in the Final EIR.

##### Rationale

Implementation of fugitive dust control plan and exhaust emissions plan would minimize emissions of criteria air pollutants during construction.

#### Section 3.9 Noise

##### Impact 3.9.1 Temporary Construction Noise

Impact 3.9.1: Construction activity would violate standards established in the local general plans or noise ordinances, and/or would adversely affect nearby sensitive receptors.

##### Mitigation

The following mitigation measure is hereby adopted and will be implemented as set forth in the MMRP. The measure will mitigate the above impact to a less than significant level.

Mitigation Measure 3.9.1: The appropriate Member Agency shall develop and implement a Construction Noise Reduction Plan that requires, at a minimum, the following:

- The contractor shall locate all stationary noise-generating equipment, including hammer bore and drill rigs, as far as possible from nearby noise-sensitive receptors. Stationary noise sources located within 500 feet of noise-sensitive receptors shall be equipped with noise reducing engine housings, and the line of sight between such sources and nearby sensitive receptors shall be blocked by portable acoustic barriers.

- The contractor shall assure that construction equipment with internal combustion engines have sound control devices at least as effective as those provided by the original equipment manufacturer. No equipment shall be permitted to have an un-muffled exhaust.

- All construction activities within unincorporated areas shall be limited to between the hours depending upon the jurisdiction.

- Residences and other sensitive receptors within 200 feet of a construction area shall be notified of the construction schedule in writing, at least two weeks prior to the commencement of construction activities. This notice shall indicate the allowable hours of construction activities as specified by the applicable local jurisdiction or as defined by this mitigation measure. The construction contractor shall designate a noise disturbance coordinator who would be responsible for responding to complaints regarding construction noise. The coordinator shall determine the cause of the complaint and ensure that reasonable measures are implemented to correct the problem. A contact number for the noise disturbance coordinator shall be conspicuously placed on construction site fences and entrances and included in the construction schedule notification sent to nearby residences and sensitive receptors.

##### Findings

Based on the EIR/EIS and the entire record before Napa County, the Board finds, in accordance with CEQA Section 15901(a)(1), that changes or alterations have been required in, or incorporated into, the project which avoid or substantially lessen the significant environmental effect as identified in the Final EIR.

##### Rationale

Construction noise levels would be limited to hours set forth in applicable noise ordinances. Construction would be short-term and temporary, therefore sensitive receptors would only be exposed to increased noise levels for a short duration.

##### Impact 3.9.2 Temporary Vibration Impacts

Impact 3.9.2: Construction activities could expose sensitive receptors to excessive ground-borne vibration levels.

##### Mitigation

The following mitigation measure is hereby adopted and will be implemented as set forth in the MMRP. The measure will mitigate the above impact to a less than significant level.

Mitigation Measure 3.9.2: The appropriate Member Agency will implement the following measure:

The construction contractor shall use a trenchless technology (e.g., horizontal directional drill, lateral drilling, etc.) other than jack and bore when there are structures within 100 feet of the proposed activities. If the construction contractor provides the Member Agency with acceptable documentation indicating that alternative trenchless technology is not feasible for the crossing, the contractor shall develop and implement a Construction Vibration Mitigation Plan to minimize construction vibration damage using all reasonable and feasible means available, including siting the jack and bore as far a possible from all nearby structures. The plan shall provide a procedure for establishing thresholds and limiting vibration values for potentially affected structures based on an assessment of each structure’s ability to withstand the loads and displacements due to construction vibrations. The plan should also include the development of a vibration monitoring plan to be implemented during construction of particular crossing.

##### Findings

Based on the EIR/EIS and the entire record before Napa County, the Board finds, in accordance with CEQA Section 15901(a)(1), that changes or alterations have been required in, or incorporated into, the project which avoid or substantially lessen the significant environmental effect as identified in the Final EIR.

##### Rationale

Most of the proposed pipelines would be installed along existing roadways and may not require use of jack and bore tunneling. In the event jack and bore tunneling would be required, the impacts from ground borne vibration would minimized by implementing a construction vibration mitigation plan.

##### Impact 3.9.3 Permanent Increases to Ambient Noise Levels

Impact 3.9.3: Operational activities could permanently generate noise levels above existing ambient levels in the vicinity of sensitive receptor locations.

##### Mitigation

The following mitigation measure is hereby adopted and will be implemented as set forth in the MMRP. The measure will mitigate the above impact to a less than significant level.

Mitigation Measure 3.9.3: The appropriate Member Agency shall implement the following measure:

- All new pump stations shall be located within enclosed structures with adequate setback and screening to achieve acceptable regulatory noise standards for industrial uses as well as to achieve acceptable levels at the property lines of nearby residences, as determine by the applicable local jurisdiction. Noise enclosures shall be designed to reduce equipment noise levels by at least 20 dBA.

##### Findings

Based on the EIR/EIS and the entire record before Napa County, the Board finds, in accordance with CEQA Section 15901(a)(1), that changes or alterations have been required in, or incorporated into, the project which avoid or substantially lessen the significant environmental effect as identified in the Final EIR.

##### Rationale

Implementation of the mitigation measure would lessen distribution and booster pump station-related noise levels that could permanently increase ambient noise levels.

#### Section 3.10 Hazardous Materials

##### Impact 3.10.1 Exposure to Hazardous Materials

Impact 3.10.1: Project construction could expose workers and the public to hazardous materials that could be present in the soil or shallow groundwater encountered during excavation.

##### Mitigation

The following mitigation measures are hereby adopted and will be implemented as set forth in the MMRP. The measures will mitigate the above impact to a less than significant level.

Mitigation Measure 3.10.1a: Project contract specifications shall require that, in the event that evidence of potential soil contamination such as soil discoloration, noxious odors, debris, or buried storage containers, is encountered during construction, the contractor will have a contingency plan for sampling and analysis of potentially hazardous substances, including use of a photoionization detector. The required handling, storage, and disposal methods shall depend on the types and concentrations of chemicals identified in the soil. Any site investigations or remediation shall comply with applicable laws and will coordinate with the appropriate regulatory agencies,

Mitigation Measure 3.10.1b: If unknown USTs are discovered during construction, the UST, associated piping, and impacted soil shall be removed by a licensed and experienced UST removal contractor. The UST and contaminated soil shall be removed in compliance with applicable county and state requirements governing UST removal.

Mitigation Measure 3.10.1c: Prepare a project-specific Health and Safety Plan that would apply to excavation activities. The plan shall establish policies and procedures to protect workers and the public from potential hazards posed by hazardous materials. The plan shall be prepared according to federal and California OSHA regulations and submitted to the appropriate agency with jurisdiction prior to beginning site activities.

Mitigation Measure 3.10.1d: Project contract specifications shall include a Dust Abatement Program to minimize potential public health impacts associated with exposure to contaminants in soil dust.

##### Findings

Based on the EIR/EIS and the entire record before Napa County, the Board finds, in accordance with CEQA Section 15901(a)(1), that changes or alterations have been required in, or incorporated into, the project which avoid or substantially lessen the significant environmental effect as identified in the Final EIR.

##### Rationale

Measures such as preparation of a health and safety plan and dust abatement program would reduce any exposure to hazardous materials during construction.

##### Impact 3.10.2 Release of Hazardous Materials

Impact 3.10.2: Project construction could increase the potential for accidental release of hazardous materials.

##### Mitigation

The following mitigation measures are hereby adopted and will be implemented as set forth in the MMRP. The measures will mitigate the above impact to a less than significant level.

Mitigation Measure 3.10.2a: Consistent with the SWPPP requirements, the construction contractor shall be required to implement BMPs for handling hazardous materials onsite. The use of construction BMPs will minimize any adverse effects on groundwater and soils, and will include, but not limited to, the following:

- Follow manufacturers’ recommendations and regulatory requirements for use, storage, and disposal of chemical products and hazardous materials used in construction;

- Spill control and countermeasures, including employee spill prevention/response training;

- Avoid overtopping construction equipment fuel gas tanks;

- During routine maintenance of construction equipment, properly contain and remove grease and oils; and

- Properly dispose of discarded containers of fuels and other chemicals.

Mitigation Measure 3.10.2b: The contractor shall follow the provisions of California Code of Regulations, Title 8, Sections 5163 through 5167 for General Industry Safety Orders to protect the action area from being contaminated by the accidental release of any hazardous materials and/or wastes. The local Certified Unified Program Agency (CUPA) will be contacted for any site-specific requirements regarding hazardous materials or hazardous waste containment or handling.

Mitigation Measure 3.10.2c: Oil and other solvents used during maintenance of construction equipment shall be recycled or disposed of in accordance with applicable regulatory requirements. All hazardous materials shall be transported handled, and disposed of in accordance with applicable regulatory requirements.

Mitigation Measure 3.10.2d: In the event of an accidental release of hazardous materials during construction, containment and clean up shall occur in accordance with applicable regulatory requirements.

##### Findings

Based on the EIR/EIS and the entire record before Napa County, the Board finds, in accordance with CEQA Section 15901(a)(1), that changes or alterations have been required in, or incorporated into, the project which avoid or substantially lessen the significant environmental effect as identified in the Final EIR.

##### Rationale

Implementation of BMPs to control usage and handling of hazardous materials and following regulatory requirements in the event of spills would reduce release of hazardous materials and any impacts associated with the release.

##### Impact 3.10.4 Wildland Fires Hazard

Impact 3.10.4: Construction activities in grassland areas could have the potential to expose people or equipment to risk of loss, injury, or death involving wildland fires.

##### Mitigation Not Applicable to Napa County.

##### Mitigation Not Applicable to SVCSD and Napa SD.

##### Mitigation Applicable to LGVSD/NMWD and Novato SD/NMWD.

The following mitigation measures are hereby adopted and will be implemented as set forth in the MMRP. The measures will mitigate the above impact to a less than significant level.

Mitigation Measure 3.10.4a: For applicable Member Agencies, in consultation with local fire agencies, a Fire Safety Plan will be developed for each of the service areas associated with the project. The Fire Safety Plan(s) will describe various potential scenarios and action plans in the event of a fire.

Mitigation Measure 3.10.4b: For applicable Member Agencies, during project construction, all staging areas, welding areas, or areas slated for development using spark-producing equipment will be cleared of dried vegetation or other material that could ignite. Any construction equipment that includes a spark arrestor shall be equipped with a spark arrestor in good working order. All vehicles and crews working at the project site(s) will have access to functional fire extinguishers at all times. In addition, construction crews will be required to have a spotter during welding activities to look out for potentially dangerous situations, including accidental sparks.

##### Findings

Based on the Final EIR/EIS and the entire record before Napa County, the Board finds, in accordance with CEQA Section 15901(a)(2), that such changes or alterations are within the responsibility and jurisdiction of another public agency and not the agency making the finding. Such changes have been adopted by such other agency or can and should be adopted by such other agency.

##### Rationale

Based on the Draft EIR/EIS, the proposed project facilities within Napa County jurisdiction would not lie within wildland fire hazard areas.

#### Section 3.11 Public Services and Utilities

##### Impact 3.11.1	Temporary Effect on Response Times for Emergency Service Providers

Impact 3.11.1: Project construction activities could temporarily affect response times for emergency service providers.

##### Mitigation

The following mitigation measure is hereby adopted and will be implemented as set forth in the MMRP. The measure will mitigate the above impact to a less than significant level.

Mitigation Measure 3.11.1: The Member Agencies will coordinate with local emergency service providers in its service area to inform them of the proposed construction activities and schedule, and provide temporary alternate access routes around construction areas as necessary.

##### Findings

Based on the EIR/EIS and the entire record before Napa County, the Board finds, in accordance with CEQA Section 15901(a)(1), that changes or alterations have been required in, or incorporated into, the project which avoid or substantially lessen the significant environmental effect as identified in the Final EIR.

##### Rationale

Coordinating with local emergency service providers would reduce any effects on the response times for emergency response during project construction.

##### Impact 3.11.2 Short-term Police and Fire Assistance

Impact 3.11.2: Project construction activities could require short-term police and fire protection services to assist in traffic management or in the event of an accident.

##### Mitigation

The following mitigation measure is hereby adopted and will be implemented as set forth in the MMRP. The measure will mitigate the above impact to a less than significant level.

Mitigation Measure 3.11.2: Public service providers shall provide, upon request, a copy of the Traffic Control Plan to the related police and fire agencies for their review prior to construction. The appropriate Member Agency shall provide 72-hour notice to the local service providers prior to construction of individual pipeline segments. Discussion on the Traffic Control Plan is provided in Section 3.7, Traffic and Circulation.

##### Findings

Based on the EIR/EIS and the entire record before Napa County, the Board finds, in accordance with CEQA Section 15901(a)(1), that changes or alterations have been required in, or incorporated into, the project which avoid or substantially lessen the significant environmental effect as identified in the Final EIR.

##### Rationale

As noted in the traffic control plan, pre-construction notice to the local service providers would reduce any impacts related to police and fire assistance during project construction.

##### Impact 3.11.3 Temporary Accidental Disruption to Utility Services

Impact 3.11.3: Project construction could result in temporary planned or accidental disruption to utility services.

##### Mitigation

The following mitigation measure is hereby adopted and will be implemented as set forth in the MMRP. This measure will mitigate the above impact to a less than significant level.

Mitigation Measure 3.11.3: The Member Agencies will identify utilities along the proposed pipeline routes and project sites prior to construction and implement the following measures:

a.	Utility excavation or encroachment permits shall be obtained as required from the appropriate agencies. These permits include measures to minimize utility disruption. The service provider and its contractors shall comply with permit conditions regarding utility disruption.

b.	Utility locations shall be verified through the use of the Underground Service Alert services and/or field survey (potholing).

c.	As necessary, detailed specifications shall be prepared as part of the design plans to include procedures for the excavation, support, and fill of areas around utility cables and pipes. All affected utility services shall be notified of construction plans and schedule. Arrangements shall be made with these entities regarding protection, relocation, or temporary disconnection of services.

d.	In areas where the pipeline would traverse parallel to underground utility lines within five feet, the project applicant shall employ special construction techniques, such as trench wall-support measures to guard against trench wall failure and possible resulting loss of structural support for the excavated areas.

e.	Residents and businesses in the project corridor shall be notified of any planned utility service disruption two to four days in advance, in conformance with county and state standards.

##### Findings

Based on the EIR/EIS and the entire record before Napa County, the Board finds, in accordance with CEQA Section 15901(a)(1), that changes or alterations have been required in, or incorporated into, the project which avoid or substantially lessen the significant environmental effect as identified in the Final EIR.

##### Rationale

Identifying utilities along the proposed pipeline routes and project sites prior to construction and executing measures to notify and coordinate with the affected utility services would minimize accidental disruption of utility services.

#### Section 3.12 Cultural Resources

##### Impact 3.12.1 Impact to Cultural Resources/Archaeological Sites

Impact 3.12.1: Project construction could affect existing cultural resources or uncover unknown and/or buried archaeological materials in areas of high prehistoric archaeological sensitivity.

##### Mitigation

The following mitigation measures are hereby adopted and will be implemented as set forth in the MMRP. The measures will mitigate the above impact to a less than significant level.

Mitigation Measure 3.12.1: The standard Section 106 process outlined at 36 CFR Part 800 will be completed prior to supplying Federal funds to be used for construction of any facilities for the project. This includes all construction money that involves whole or in partial financing and includes both payment in advance or in reimbursement.

If project circumstances are such that it is infeasible to implement the measures identified below, a phased identification and evaluation strategy that accounts for the individual project effects will be developed in accordance with the procedures for doing so detailed in 36 CFR Part 800.4(b)(2). The alternative procedures would provide a similar level of accounting regarding the effects to cultural resources in a manner not inconsistent with the standard process provided for at 36 CFR Part 800. The alternative procedures agreed to in the Programmatic Agreement would need to be completed prior to construction of any actions that are subsidized with Federal funds. Pursuant to the Section 106 process, the appropriate Member Agency will incorporate the following measures:

Mitigation Measure 3.12.1a: Prepare a Cultural Resources Monitoring Plan. Prior to authorization to proceed, or issuance of permits, the applicant shall prepare and submit a cultural resources monitoring plan to the appropriate jurisdiction for review and approval. Monitoring shall be required for all surface alteration and subsurface excavation work including trenching, boring, grading, use of staging areas and access roads, and driving vehicles and equipment within all areas delineated as sensitive for cultural resources. A qualified professional archaeologist (cultural resources monitor) that is approved by each Member Agency in consultation with all affected jurisdictions shall prepare the plan. The plan shall address (but not be limited to) the following issues:

- Training program for all construction and field workers involved in site disturbance;

- Person(s) responsible for conducting monitoring activities, including Native American monitors;

- How the monitoring shall be conducted and the required format and content of monitoring reports, including any necessary archaeological re-survey of the final pipeline alignment (including the need to conduct shovel-test units or auger samples to identify deposits in advance of construction), assessment, designation and mapping of the sensitive cultural resource areas on final project maps, assessment and survey of any previously unsurveyed areas;

- Person(s) responsible for overseeing and directing the monitors;

- Schedule for submittal of monitoring reports and person(s) responsible for review and approval of monitoring reports;

- Procedures and construction methods to avoid sensitive cultural resource areas (i.e. boring conduit underneath recorded or discovered cultural resource site);

- Clear delineation and fencing of sensitive cultural resource areas requiring monitoring;

- Physical monitoring boundaries (e.g., 200-foot radius of a known site);

- Protocol for notifications in case of encountering of cultural resources, as well as methods of dealing with the encountered resources (e.g., collection, identification, curation);

- Methods to ensure security of cultural resources sites;

- Protocol for notifying local authorities (i.e. Sheriff, Police) should site looting and other illegal activities occur during construction.

Mitigation Measure 3.12.1b: Archaeological and Native American Monitoring. If an intact archaeological deposit is encountered, all soil disturbing activities in the vicinity of the deposit shall cease until the deposit is evaluated. The appropriate Member Agency, as necessary, shall retain the services of a Native American monitor and a qualified archaeological consultant that has expertise in California prehistory to monitor ground-disturbing within areas designated as being sensitive for buried cultural resources. The archaeological monitor shall immediately notify the appropriate Member Agency of the encountered archaeological deposit. The monitors shall, after making a reasonable effort to assess the identity, integrity, and significance of the encountered archaeological deposit, present the findings of this assessment to NBWRA and the appropriate Member Agency. During the course of the monitoring, the archaeologist may adjust the frequency—from continuous to intermittent—of the monitoring based on the conditions and professional judgment regarding the potential to impact resources.

If a Member Agency, in consultation with the monitors, determines that a significant archaeological resource is present within their jurisdiction and that the resource could be adversely affected by the NBWRP, the Member Agency shall:

- Re-design the NBWRP to avoid any adverse effect on the significant archaeological resource; or,

- Implement an archaeological data recovery program (ADRP) (unless the archaeologist determines that the archaeological resource is of greater interpretive than research significance and that interpretive use of the resource is feasible). If the circumstances warrant an archaeological data recovery program, an ADRP shall be conducted. The project archaeologist and the Member Agency shall meet and consult to determine the scope of the ADRP. The archaeologist shall prepare a draft ADRP that shall be submitted to the appropriate Member Agency for review and approval. The ADRP shall identify how the proposed data recovery program would preserve the significant information the archaeological resource is expected to contain. The ADRP shall identify the scientific/historic research questions applicable to the expected resource, the data classes the resource is expected to possess, and how the expected data classes would address the applicable research questions. Data recovery, in general, shall be limited to the portions of the historic property that could be adversely affected by the NBWRP. Destructive data recovery methods shall not be applied to portions of the archaeological resources if nondestructive methods are practical.

Mitigation Measure 3.12.1c: Cultural Resources Assessment for Staging Areas. When locations for staging are defined the areas of potential effect should be subject to a cultural resources investigation that includes, at a minimum:

- An updated records search at the Northwest Information Center;

- An intensive survey of all areas within the lots;

- A report disseminating the results of this research; and,

- Recommendations for additional cultural resources work necessary to mitigate any adverse impacts to recorded and/or undiscovered cultural resources.

Mitigation Measure 3.12.1d: Inadvertent Discoveries. If discovery is made of items of historical or archaeological interest, the contractor shall immediately cease all work activities in the area (within approximately 100 feet) of discovery. Prehistoric archaeological materials might include obsidian and chert flaked-stone tools (e.g., projectile points, knives, scrapers) or toolmaking debris; culturally darkened soil (“midden”) containing heat-affected rocks, artifacts, or shellfish remains; and stone milling equipment (e.g., mortars, pestles, handstones, or milling slabs); and battered stone tools, such as hammerstones and pitted stones. Historic-period materials might include stone, concrete, or adobe footings and walls; filled wells or privies; and deposits of metal, glass, and/or ceramic refuse. After cessation of excavation the contractor shall immediately contact the NBWRA and appropriate Member Agency. The contractor shall not resume work until authorization is received from the appropriate Member Agency.

- In the event of unanticipated discovery of archaeological indicators during construction, the Member Agency shall retain the services of a qualified professional archaeologist to evaluate the significance of the items prior to resuming any activities that could impact the site.

- In the case of an unanticipated archaeological discovery, if it is determined that the find is unique under the National Historic Preservation Act (NHPA) and/or potentially eligible for listing in the National Register, and the site cannot be avoided, appropriate Member Agency shall provide a research design and excavation plan, prepared by an archaeologist, outlining recovery of the resource, analysis, and reporting of the find. The research design and excavation plan shall be submitted to NBWRA and appropriate Member Agency and approved by the appropriate Member Agency prior to construction being resumed.

Mitigation Measure 3.12.1e: Project-level Cultural Resources Assessment. When project-level plans are completed for the Basic System; the Partially Connected System; and the Fully Connected System, NBWRA the appropriate Member Agency will conduct a cultural resources investigation for the APE that includes, at a minimum:

- An updated records search at the Northwest Information Center (NWIC);

- An intensive cultural resources survey of the Area of Potential Effect (APE);

- A report disseminating the results of this research; and,

- Recommendations for additional cultural resources work necessary to mitigate any adverse impacts to recorded and/or undiscovered cultural resources.

##### Findings

Based on the EIR/EIS and the entire record before Napa County, the Board finds, in accordance with CEQA Section 15901(a)(1), that changes or alterations have been required in, or incorporated into, the project which avoid or substantially lessen the significant environmental effect as identified in the Final EIR.

##### Rationale

Measures such Section 106 consultation and monitoring of cultural resources, archaeological and Native American sites, and cultural resource assessment would minimize impacts to the sites.

##### Impact 3.12.2 Discovery of Human Remains

Impact 3.12.2: Project construction could result in damage to previously unidentified human remains.

##### Mitigation

The following mitigation measures are hereby adopted and will be implemented as set forth in the MMRP. The measures will mitigate the above impact to a less than significant level.

Mitigation Measure 3.12.2: Discovery of Human Remains. If potential human remains are encountered, the appropriate Member Agency shall halt work in the vicinity of the find and contact the county coroner in accordance with Public Resources Code Section 5097.98 and Health and Safety Code Section 7050.5. If the coroner determines the remains are Native American, the coroner shall contact the Native American Heritage Commission (NAHC). As provided in Public Resources Code Section 5097.98, the NAHC shall identify the person or persons believed to be most likely descended from the deceased Native American. The most likely descendent makes recommendations for means of treating or disposing of, with appropriate dignity, the human remains and any associated grave goods as provided in Public Resources Code Section 5097.98.

##### Findings

Based on the EIR/EIS and the entire record before Napa County, the Board finds, in accordance with CEQA Section 15901(a)(1), that changes or alterations have been required in, or incorporated into, the project which avoid or substantially lessen the significant environmental effect as identified in the Final EIR.

##### Rationale

In the inadvertent discovery of human remains, work would halted and the mitigation would include notifying the NAHC and the most likely descendants would recommend the means of treating and disposing the remains.

#### Section 3.13 Recreation

##### Impact 3.13.1 Temporary Disturbance

Impact 3.13.1: Project construction could result in short-term disturbance adjacent to recreational facilities.

##### Mitigation

The following mitigation measures are hereby adopted and will be implemented as set forth in the MMRP. These measures will mitigate the above impact to a less than significant level.

Mitigation Measure 3.13.1a: The appropriate Member Agency shall coordinate with the appropriate local and regional agencies to identify detour routes for the bikeways and trails during construction where feasible, as part of the Traffic Control/Traffic Management Plan (see Measure 3.11.1a).

Mitigation Measure 3.13.1b: Implement Mitigation Measures 3.8-1a through 3.8.1b, Mitigation Measures 3.9.1 through 3.9-3.

Mitigation Measure 3.13.2: Before beginning construction, the contractor will develop, in consultation with the appropriate representative(s) of the affected park’s managing agency, a plan indicating how public access to the park will be maintained during construction. If needed, flaggers will be stationed near the construction activity area to direct and assist members of the public around the activity areas while maintaining access to the parks.

##### Findings

Based on the EIR/EIS and the entire record before Napa County, the Board finds, in accordance with CEQA Section 15901(a)(1), that changes or alterations have been required in, or incorporated into, the project which avoid or substantially lessen the significant environmental effect as identified in the Final EIR.

##### Rationale

Coordination with the local agencies and consulting local park management agency prior to construction would minimize any disturbance to recreational facilities.

#### Section 3.14 Aesthetics

##### Impact 3.14.1 Temporary Impact to Scenic Vista

Impact 3.14.1: NBWRP construction activities could temporarily affect scenic vistas or corridors in the NBWRP area.

##### Mitigation

The following mitigation measures are hereby adopted and will be implemented as set forth in the MMRP. The measures will mitigate the above impact to a less than significant level.

Mitigation Measure 3.14.1a: Following construction activities, disturbed areas shall be restored to baseline conditions, including repaving roadways, replanting trees, and/or reseeding with a native seed mix typical of the immediately surrounding area.

Mitigation Measure 3.14.1b: Berms around constructed reservoirs shall be vegetated with native seed mixes to soften the visual effect of the reservoirs from adjacent roadways.

Mitigation Measure 3.14.1c: Design elements shall be incorporated to enhance visual integration of the booster pump station and distribution pump station with their surroundings. Proposed facilities shall be painted low-glare earth-tone colors that blend with the surrounding terrain. Highly reflective building materials and/or finishes shall not be used in the designs for proposed facilities.

##### Findings

Based on the EIR/EIS and the entire record before Napa County, the Board finds, in accordance with CEQA Section 15901(a)(1), that changes or alterations have been required in, or incorporated into, the project which avoid or substantially lessen the significant environmental effect as identified in the Final EIR.

##### Rationale

Temporary effects to scenic vistas would be minimized by restoring the areas to pre-existing conditions and incorporating design elements to integrate the project components with the surroundings.

##### Impact 3.14.2 Impact to Views Along Scenic Roadways

Impact 3.14.2: Implementation of NBWRP could affect views along eligible or designated Caltrans Scenic Highways, or locally-defined scenic routes.

##### Mitigation

The following mitigation measures are hereby adopted and will be implemented as set forth in the MMRP. The measures will mitigate the above impact to a less than significant level.

The appropriate Member Agency will implement the following measures:

Mitigation Measure 3.14.1a (identified above)
Mitigation Measure 3.14.1b (identified above)

##### Findings

Based on the EIR/EIS and the entire record before Napa County, the Board finds, in accordance with CEQA Section 15901(a)(1), that changes or alterations have been required in, or incorporated into, the project which avoid or substantially lessen the significant environmental effect as identified in the Final EIR.

##### Rationale

Implementation of measures to minimize effects on scenic vista would also lessen the impacts to views along scenic roadways.

##### Impact 3.14.3 Source of Light or Glare

Impact 3.14.3: NBWRP components could introduce new sources of light and glare on the project sites.

##### Mitigation

The following mitigation measures are hereby adopted and will be implemented as set forth in the MMRP. The measures will mitigate the above impact to a less than significant level.

Mitigation Measure 3.14.3a: The exterior lighting installed around the operational and capacity storage reservoirs, distribution pump station, storage tanks, and booster pump station shall be of a minimum standard required to ensure safe visibility. Lighting also shall be shielded and directed downward to minimize impacts of light and glare.

Mitigation Measure 3.14.3b: All exterior lighting is directed downward and oriented to insure that limited light source is directly visible from neighboring residential areas. If necessary, landscaping would be provided around proposed facilities. The vegetation would be selected, placed, and maintained to minimize off-site light and glare onto surrounding areas.

Mitigation Measure 3.14.1c: Design elements shall be incorporated to enhance visual integration of the booster pump station and distribution pump station with their surroundings. Proposed facilities shall be painted low-glare earth-tone colors that blend with the surrounding terrain. Highly reflective building materials and/or finishes shall not be used in the designs for proposed facilities.

##### Findings

Based on the EIR/EIS and the entire record before Napa County, the Board finds, in accordance with CEQA Section 15901(a)(1), that changes or alterations have been required in, or incorporated into, the project which avoid or substantially lessen the significant environmental effect as identified in the Final EIR.

##### Rationale

Exterior lighting for the proposed components would be designed and installed to reduce the glare.

##### Impact 3.14.4 Long-term Impact to Aesthetic Character

Impact 3.14.4: Development of the proposed facilities, particularly pump stations and storage reservoirs, would permanently alter the aesthetic character of the action area.

##### Mitigation

The following mitigation measures are hereby adopted and will be implemented as set forth in the MMRP. The measures will mitigate the above impact to a less than significant level.

Mitigation Measure 3.14.4a: After construction of any facility that is above grade and visible to sensitive receptors, visual screening and vegetation measures will be implemented to reduce impacts to scenic views. Trees or other suitable vegetation along the fenceline of the facility should be incorporated to reduce the industrial appearance of the structures. Similarly, berms for new storage ponds or pond reconfiguration will be re-vegetated to reduce the barren appearance of the berms.

Mitigation Measure 3.14.4b: Dark colored, non-reflective building materials should be used for project components that cause potentially significant impact from glare to visual resources.

##### Findings

Based on the EIR/EIS and the entire record before Napa County, the Board finds, in accordance with CEQA Section 15901(a)(1), that changes or alterations have been required in, or incorporated into, the project which avoid or substantially lessen the significant environmental effect as identified in the Final EIR.

##### Rationale

Designing the project elements to provide visual screening or using non-reflecting building materials would not have a significant effect to the existing aesthetic character.

#### Chapter 4 Cumulative Impacts

##### Impact 4.1 Wastewater Treatment Capacity

Impacts 4.1: Construction-related Cumulative Impacts. Concurrent construction of several projects within the Sonoma, Napa, and Marin County areas could result in cumulative short-term impacts associated with construction activities. If implemented at the same time as other construction projects, construction of facilities under all three of the alternatives could contribute to potential short-term cumulative effects associated with erosion, cultural resource disturbance, disturbance of adjacent land uses, traffic disruption, dust generation, construction noise, aesthetics, air quality, biological resources, hazardous materials, water quality, public services and utilities. However, construction-related impacts would not result in long term alteration of the environment, and could be mitigated to less than significant levels through the use of mitigation measures identified throughout Chapter 3 (of the Draft EIR/EIS).

##### Mitigation

The following mitigation measure is hereby adopted and will be implemented as set forth in the MMRP. The measure will mitigate the above impact to a less than significant level.

Mitigation Measure 4.1: Member Agencies shall coordinate construction activities along selected alignments to identify overlapping pipeline routes, project areas, and construction schedules. To the extent feasible, construction activities shall be coordinated to consolidate the occurrence of short-term construction-related impacts.

##### Findings

Based on the EIR/EIS and the entire record before Napa County, the Board finds, in accordance with CEQA Section 15901(a)(1), that changes or alterations have been required in, or incorporated into, the project which avoid or substantially lessen the significant environmental effect as identified in the Final EIR.

##### Rationale

Due to their short-term nature and the inclusion of appropriate mitigation measures as established in Chapter 3 of the Draft EIR/EIS, NBWRP’s contribution to cumulative impacts on wastewater treatment capacity is not considerable.

##### Impact 4.5 Cumulative Long-term Impacts on Biological Resources

Impact 4.5: Concurrent construction of the NBWRP with other projects proposed in the Sonoma, Napa, and Marin County area, and other water and wastewater infrastructure projects, could result in cumulative long-term impacts to biological resources.

##### Mitigation

Implement Measures 3.5.1 through 3.5.14. The following mitigation measures are hereby adopted and will be implemented as set forth in the MMRP.

##### Findings

Based on the EIR/EIS and the entire record before Napa County, the Board finds, in accordance with CEQA Section 15901(a)(1), that changes or alterations have been required in, or incorporated into, the project which avoid or substantially lessen the significant environmental effect as identified in the Final EIR.

##### Rationale

Mitigation measures for protection of the biological resources would minimize project impacts and its contribution to cumulative impacts to less than cumulatively considerable.

# Footnotes

Setbacks of channels with associated riparian vegetation will be from the outer dripline edge of the riparian corridor canopies and/or the upper bank edge, or per City or County code, whichever is greater.